## Slide 1: VERIFICATION OF Ethernet MAC LAYER
Graduation Project Final Discussion
sponsored By : PYRAMIDTECH DR. Ahmed Abou-Auf
DR. Mostafa Ghouneem
Eng. ALI Maher

## Slide 2: Team members
Nada Yehia Elsayed
Mohammad Wael Monir
Mariam Hossam Abd-Elghaffar
Muhammad Majid Abdul-Halim
Mounir Essam Mounir

## Slide 3: agenda
Introduction to Ethernet Protocol
Ethernet MAC IP
Ethernet UVM Architecture
TX Operation
TX Verification
RX Operation
RX Verification
Control Verification
MII Operation
MII Verification
Code Coverage
Future work

## Slide 4: INTRODUCTION TO ETHERNET Protocol

## Slide 5: Introduction to Ethernet
Ethernet is the most widely used wired Local Area Network (LAN) technology, standardized by IEEE 802.3.
Key Features:
  Operates at the Physical (Layer 1) and Data Link (Layer 2) of the OSI model.
  Supports multiple data rates, including 10 Mbps, 100 Mbps, 1 Gbps, and higher

## Slide 6: Ethernet MAC IP

## Slide 7: Ethernet MAC IP
  The Ethernet MAC is the lower sublayer of Layer 2 that interfaces higher-layer protocols with the Ethernet physical layer.
  This project verifies the open-source Ethernet MAC IP from OpenCores

## Slide 8: Ethernet UVM Architecture

## Slide 9: Ethernet UVM Architecture

## Slide 10: Ethernet UVM Components
Models the external memory that the DUT accesses via its WISHBONE master port.
The DUT initiates every transaction.
Wishbone Master Agent (Reactive)

## Slide 11: Ethernet UVM Components
Models the host processor (RISC/CPU) that configures the MAC.
The testbench initiates all transactions.
Wishbone Slave Agent (Active)

## Slide 12: Ethernet UVM Components
Simulates the Ethernet PHY transmitter interface.
Includes a monitor to capture transmitted frames by the DUT.
MII Tx Agent (Active)

## Slide 13
Simulates the Ethernet PHY receiver interface.
Sends Ethernet frames to the DUT through the MII RX interface.
MII Rx Agent (Active)
Ethernet UVM Components

## Slide 14: Ethernet UVM Components
Models the PHY chip on the MDIO management interface.
Initiates all MII management transactions for configuration and status read of the physical device.
MDIO Agent (Active)

## Slide 15: Ethernet UVM Components
Controls the RST_I signal to the DUT independently of any other sequence.
Drives RST_I high/low for programmable durations
Reset Agent (Active)

## Slide 16: Register Abstraction Layer (RAL)
RAL provides an easy and organized way to access and verify DUT registers and buffer descriptors.

## Slide 17: TX Operation

## Slide 18: Basic frame transmission

## Slide 19: Half Duplex

## Slide 20: TX Verification

## Slide 21: Verification Plan
We put test plan for testing this features
All TX configurations (full/half duplex CRC, PAD,…etc)
Interframe gap time
Corner cases (Limits of frame length, retry count,…etc)
Errors (Huge frame, Underrun,…etc)
30 Constraint randomized test cases

## Slide 22: Verification Architecture

## Slide 23: TX Scoreboard

## Slide 24: Bugs & Functional Coverage
Functional Coverage

## Slide 25: RX Operation

## Slide 26: Basic Frame Reception

## Slide 27: rX Verification

## Slide 28
Reserved |  |  |  |  |  |  |  |  |  |  |  |  |  |  | RECSMALL
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16
PAD | HUGEN | CRCEN | DLYCRCEN | Reserved | FULLD | EXDFREN | NOBCKOF | LOOPBCK | IFG | PRO | IAM | BRO | NOPRE | TXEN | RXEN
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Configuration Registers
MODER Register

## Slide 29
RX Buffer Descriptor
LEN | E | IRQ | WR | Reserved | CF | M | OR | IS | DN | TL | SF | CRC | LC
31:16 | 15 | 14 | 13 | 12:9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
RXPNT [31:0] – Pointer to buffer in memory

## Slide 30
Verification Plan
➢ All RX MODER configurations
(PRO, BRO, IAM, HUGEN, RECSMALL, RXEN).
➢ Address Recognition & Filtering combinations
(Exact Match, Unicast Miss, Broadcast, and Multicast Hash).
➢ Corner cases & Frame Boundaries
(MINFL logic with RECSMALL, MAXFL truncation vs. Jumbo frames).
➢ Error Injection & Robustness Testing
(Single-bit/Multi-bit MAC address mismatches, Byte Reversal).
➢ Extensive Constrained-random test sequences to cross-cover all feature combinations.
We developed a comprehensive test plan targeting these RX features:

## Slide 31: RX ARCHITECTURE
RAL Model
Rx Scoreboard
Registers
Buffer Descriptor
DMA
PHY
WB Slave Agent
WB Master Agent
MII Rx Agent
WB S Driver
WB S Monitor
WB M Driver
WB M Monitor
MII Rx Driver
Ethernet Frame
MII Rx Monitor
MII Rx Sequencer
DUT
if

## Slide 32: RX ARCHITECTURE
RAL Model
Rx Scoreboard
Registers
Buffer Descriptor
DMA
PHY
WB Slave Agent
WB Master Agent
MII Rx Agent
WB S Driver
WB S Monitor
WB M Driver
WB M Monitor
MII Rx Driver
MII Rx Monitor
MII Rx Sequencer
DUT
if
Ethernet Frame

## Slide 33: RX ARCHITECTURE
RAL Model
Rx Scoreboard
Registers
Buffer Descriptor
DMA
PHY
WB Slave Agent
WB Master Agent
MII Rx Agent
WB S Driver
WB S Monitor
WB M Driver
WB M Monitor
MII Rx Driver
MII Rx Monitor
MII Rx Sequencer
DUT
if
Ethernet Frame

## Slide 34: RX ARCHITECTURE
RAL Model
Rx Scoreboard
Registers
Buffer Descriptor
DMA
PHY
WB Slave Agent
WB Master Agent
MII Rx Agent
WB S Driver
WB S Monitor
WB M Driver
WB M Monitor
MII Rx Driver
MII Rx Monitor
MII Rx Sequencer
DUT
if
Ethernet Frame

## Slide 35: RX ARCHITECTURE
RAL Model
Rx Scoreboard
Registers
Buffer Descriptor
DMA
PHY
WB Slave Agent
WB Master Agent
MII Rx Agent
WB S Driver
WB S Monitor
WB M Driver
WB M Monitor
MII Rx Driver
MII Rx Monitor
MII Rx Sequencer
DUT
if
Ethernet Frame
Reconstructed Eth Frame

## Slide 36
RAL Model
Rx Scoreboard
Registers
Buffer Descriptor
DMA
PHY
WB Slave Agent
WB Master Agent
MII Rx Agent
WB S Driver
WB S Monitor
WB M Driver
WB M Monitor
MII Rx Driver
MII Rx Monitor
MII Rx Sequencer
DUT
if
Ethernet Frame
Reconstructed Eth Frame

## Slide 38
RAL Model
Registers
Buffer Descriptor
DMA
PHY
WB Slave Agent
WB Master Agent
MII Rx Agent
WB S Driver
WB S Monitor
WB M Driver
WB M Monitor
MII Rx Driver
MII Rx Monitor
MII Rx Sequencer
DUT
if
Comparator
Predictor
MII Rx FIFO
Payload Queue
MII Rx FIFO

## Slide 39: BUG
✅Expected: LEN = 512 | TL = 1
❌Actual: LEN = 0 | TL = 0
Receiving Oversized Frame (HUGEN=0)
IS
ByteCnt = MaxFL
(512)
Reset Counter
ByteCnt drops to 0
Check: Is ByteCnt > 512 ?
512 > 512 ➡️ FALSE
TL Bit remains 0
Reset Logic
Status Logic
End of Frame ➡️ Write to BD
Actual Result: LEN = 0, TL = 0

## Slide 40: BUG
0000 0000 0000 0000 0100 0000 0000 0010

## Slide 41: Functional Coverage

## Slide 42: Control Verification

## Slide 43: Verification Plan
We put test plan for testing this features
All Control Moder configurations (TXFLOW, RXFLOW, PASSALL, Interrupts…etc).
Verify PAUSE Timer Functionality.
Corner cases (Limits of frame length, delay CRC,…etc).
Error Injection & Robustness Testing
Constraint randomized test cases

## Slide 44
Sending Pause Control Frame
Host Send Request TPAUSERQ =1
TX Active?
Control Tackes Over
(TX-MAC)
Start Control Frame.
(TXStartFrm)
PAD + FCS
Wait for current transmission to end
NO
Yes
Transmit through PHY
Signal Completion
(TXEndFrm)
Release
Request Latch
TPAUSERQ = 0
Frame Sent. Ready for new frame
Destination Add.
Source Add.
Type
0x8808
Opcode
0x0001
Pause time
Reserved/Padding
FCS
Generated Pause Control Frame (64 Bytes)
6 Bytes
6 Bytes
2 B
2 B
2 B
42 Bytes
4 Bytes
Enable and Configuration: Set CTRLMODER (TXFLOW) then Write TXCTRL with TXPAUSETV and PAUSE request

## Slide 45
Receiving Pause Control Frame
Incoming frame from PHY
Valid Pause frame
DA=01-80-C2-00-00-01 or own MAC
Type = 0x8808, Opcode = 0x0001
CTRLMODER.RXFLOW = 1?
Load Pause Timer
Set Interrupt RXC
TX MAC Paused
Timer Reach 0 (TX Resume)
Normal Data Frame
TX not Blocked
PASSALL =1
Store to Memory
Store frame
BD.CF = 1
NO
NO
Yes
Yes
PASSALL = 1
Store Frame
BD.CF = 1
Yes
NO
YES
Dropped
NO
Set Interrupt RXB
Only RXC fires not RXB

## Slide 46
Problems & Solutions in RX
1: Inject error and drive it to scoreboard
2: Frame synchronization.
3: Control Frame synchronization.
4: Reset Payload after each frame.

## Slide 47
Problems & Solutions in RX
1: Inject error and drive it to scoreboard
2: Frame synchronization.
3: Control Frame synchronization.
4: Reset Payload after each frame.

## Slide 48: BUGS

## Slide 49: MII Operation

## Slide 50: Scope & Objective
Scope: DUT files under test
  eth_miim.v
    eth_clockgen.v
    eth_shiftreg.v
    eth_outputcontrol.v
Objective: reach 100% functional coverage, maximize code coverage

## Slide 51: MII Verification

## Slide 52: TestbencH Architecture

## Slide 53: Test Suite Overview
15 test cases, divided mainly in three categories:
  Reset & Clock Generation
  Writing to PHY
  Reading From PHY
Target:
  Protocol correctness
  Register/priority edge cases
  Timing/corner-case

## Slide 54: Functional Coverage Results
MIIM Functional Coverage:

## Slide 55: RTL Bugs
MIIM-Bug-001:
  Description: In-flight MIIM operation abort permanently deadlocks Busy.
  Severity: High.
  Root Cause: Nvalid signal is left set with no path to 0.
    Busy = ... | InProgress | InProgress_q3 | Nvalid;
  Trigger: Normal register write
  Recovery: only a full core reset clears it.

## Slide 56: CODE COVERAGE

## Slide 57: Code Coverage
Reasons for Not Achieving 100% Coverage:
  Unreachable code in RTL.
  Reserved bits in the Register file.
  Need for direct test cases.
Before Exclusion
After Exclusion

## Slide 58: Future work

## Slide 59: Future Work
Implement direct test cases to achieve higher code coverage.
Back-to-Back (B2B) configuration: connecting two instances of the DUT/environment directly to each other.

## Slide 60: Thank you