## Slide 1: MIIM Verification

## Slide 2: Scope & Objective
Scope: DUT files under test
  eth_miim.v
    eth_clockgen.v
    eth_shiftreg.v
    eth_outputcontrol.v
Objective: reach 100% functional coverage, maximize code coverage

## Slide 3: TestbencH Architecture

## Slide 4: Test Suite Overview
21 directed test cases, divided mainly in three categories:
  Reset & Clock Generation
  Writing to PHY
  Reading From PHY
Target:
  Protocol correctness
  Register/priority edge cases
  Timing/corner-case

## Slide 5: Functional & Code Coverage Results
MIIM Functional Coverage:
MIIM Code Coverage:

## Slide 6: RTL Bugs
MIIM-Bug-001:
  Description: In-flight MIIM operation abort permanently deadlocks Busy.
  Severity: High.
  Root Cause: Nvalid signal is left set with no path to 0.
    Busy = ... | InProgress | InProgress_q3 | Nvalid;
  Trigger: Normal register write
  Recovery: only a full core reset clears it.

## Slide 7: RTL Notes
MIIM-RTL-NOTE-001:
  Description: in eth_clockgen.v, CounterPreset[7] structurally unreachable.
  Severity: N/A (not a bug), unused resources.
  Reason: max value of CounterPreset is 126, This is a dead bit by design.

## Slide 8: Open Items
MIIM-RTL-NOTE-002:
  Description: Prsd[15] / LinkFail read back incorrect via WB register interface.
  Severity: Medium (data-integrity, not a hang).
  Status: Open/unresolved.